## Slide 1
IMAGE SENSOR ENGINEERING
CCD vs CMOS Sensors
A Technical Comparison of Architecture, Performance, and Engineering Trade-offs
CCD
CMOS
Presented by P. Akhila [192472320] B. Priyanga [192511102] P. Akhila [192425225] K. Ruchitha [192472299] M. Thanuja [192425356] S. Varsha [192572177]

## Slide 2
AGENDA
What We'll Cover
01
Sensor Fundamentals
How photons become a digital image in both technologies
02
Architecture & Signal Path
Charge transfer vs. active pixel readout
03
Technical Parameter Comparison
Noise, dynamic range, speed, power, cost
04
Performance Benchmarks
Quantified trade-offs across key metrics
05
Engineering Trade-offs & Applications
Where each sensor architecture wins
06
Selection Guidance
Matching sensor type to system requirements
CCD vs CMOS Image Sensors
2

## Slide 3
FUNDAMENTALS
A Shared Starting Point, A Different Path
Both technologies use silicon photodiodes to convert incoming photons into electrical charge. They diverge entirely in how that charge is measured and read out.
Photon
Capture
→
Charge
Generation
→
Charge → Voltage
Conversion
→
Amplification
& Readout
→
Digitization
(ADC)
Where the divergence begins →
CCD — Charge-Coupled Device
Charge is physically shifted, pixel by pixel, through the silicon substrate to a single output node.
Only one (or a few) high-precision amplifier converts charge to voltage for the entire array.
Analogous to a “bucket brigade” passing charge packets down a line.
CMOS — Active Pixel Sensor
Each pixel integrates its own amplifier (and often ADC), converting charge to voltage on-site.
Pixels are addressed like memory cells — rows and columns selected electronically.
Enables massively parallel, high-speed readout across the array.
CCD vs CMOS Image Sensors
3

## Slide 4
ARCHITECTURE — CCD
CCD Signal Path: Sequential Charge Transfer
Photodiode array
Vertical shift registers move charge
down, row by row, into the horizontal
shift register (bottom row).
Horizontal
Shift Register
→
Single Output
Amplifier
→
Correlated
Double Sampling
→
ADC
Engineering consequence
Every pixel is read through the same amplifier → excellent pixel-to-pixel uniformity and low fixed-pattern noise.
Serial transfer of the entire frame → slower readout and higher clocking power (multiple drive voltages, ~15–30V).
CCD vs CMOS Image Sensors
4

## Slide 5
ARCHITECTURE — CMOS
CMOS Signal Path: Parallel Pixel-Level Readout
Each pixel = photodiode + amplifier
Row and column decoders address
pixels electronically — no physical
charge transfer between pixels.
Row / Column
Decoders
→
Per-Column
ADC Bank
→
Digital Signal
Processing
→
Digital
Output
Engineering consequence
Parallel, column-level ADCs → dramatically faster frame rates and much lower power (single low-voltage supply).
Per-pixel amplifier variation → higher fixed-pattern noise, mitigated by correlated double sampling (CDS).
CCD vs CMOS Image Sensors
5

## Slide 6
TECHNICAL COMPARISON
Key Parameters, Side by Side
Parameter
CCD
CMOS
Readout architecture
Serial, single output amplifier
Parallel, per-pixel / per-column
Typical readout speed
Lower (tens of fps, frame-limited)
High (hundreds of fps achievable)
Power consumption
High (multiple clock voltages)
Low (single supply, ~1/3–1/10 of CCD)
Read / dark noise
Very low, highly uniform
Higher, improving with CDS designs
Dynamic range
High, typically >70 dB
Moderate–high, 60–75 dB (design-dependent)
Fill factor
Near 100% (front-illuminated)
Lower natively; recovered via microlenses
Blooming / smear
Susceptible to charge overflow
Minimal — pixels reset independently
Shutter type
Native global shutter
Rolling shutter common; global shutter costs area
Fabrication
Specialized, low-volume process
Standard CMOS fabs — high volume, low cost
On-chip integration
Sensor only; external support ICs
ADC, timing, and logic integrated (SoC)
CCD vs CMOS Image Sensors
6

## Slide 7
BENCHMARKS
Relative Performance Across Key Metrics
Illustrative index scores (0–10, higher is better) reflecting typical, design-dependent behavior — not fixed physical constants.
Chart: 
| Noise Performance | Dynamic Range | Readout Speed | Power Efficiency | Fill Factor | Manufacturing Cost Efficiency
CCD | 9 | 9 | 4 | 3 | 9 | 4
CMOS | 6.5 | 7 | 9 | 9 | 6 | 9
CCD vs CMOS Image Sensors
7

## Slide 8
TRADE-OFFS & APPLICATIONS
Where Each Architecture Wins
CCD — Precision over Speed
Best fit when:
Absolute image quality and uniformity outweigh speed or power budget
Very low light levels demand minimal noise (astronomy, spectroscopy)
Scientific / metrology imaging needs precise, repeatable pixel response
High-end machine vision and some medical imaging (X-ray, microscopy)
CMOS — Speed, Power & Integration
Best fit when:
High frame rates, low power, and compact system integration are priorities
Battery-powered or space-constrained devices (smartphones, wearables)
Real-time, high-speed capture is required (automotive, robotics, sports)
Cost-sensitive, high-volume production (consumer electronics, security)
CCD vs CMOS Image Sensors
8

## Slide 9
CONCLUSION
The Engineering Verdict
Neither architecture is universally superior — the choice is a systems-engineering trade-off between image fidelity and speed / power / cost.
CCD
Choose for uncompromising image quality where power and speed are secondary.
Superior noise & uniformity
Native global shutter
Higher power & cost, slower readout
CMOS
Choose for speed, power efficiency, integration, and cost at scale.
High speed, low power, on-chip SoC
Low-cost, high-volume fabrication
Historically higher noise; now closing the gap
CCD vs CMOS Image Sensors
9